DEVELOPMENT CONTROL DEPARTMENT

CHECKLIST FOR BUILDING PLAN ON POLLUTION CONTROL

(A guide to check BP on Pollution Control)

Proposal	:    ________________________________________________________________

BP No.	:    ________________________________________________________________

| S/N | Item | Yes | No | N.A. | Remarks |
| --- | --- | --- | --- | --- | --- |
| General |
| 1 | Is the Project Reference Number and Plan Type (e.g. BP001, BP002, etc.) indicated on all the plans submitted? | ( | ( | ( | If No, please clearly indicate on the plans. |
| 2 | Are the plans on pollution control endorsed by the QP? | ( | ( | ( | If No, QP shall ensure and acknowledge that: “All relevant requirements and provisions as stipulated in the Environmental Protection and Management Act and the Code of Practice for Pollution Control (i.e. SS 593: 2013) shall be complied with.” |
| 3 | Have you consulted DCD on the use of industrial premises? | ( | ( | ( | For Industrial development, the QP/developer/owner should consult DCD prior to DC submission. If No, please submit the application form online via the Industrial Allocation System (IAS). The website address for the IAS is https://e-services.nea.gov.sg/IAS/PublicApplicant/Homepage.aspx. If NA, please provide reason to support that IA application is not required for the proposed development. |
| 4 | Has DC clearance been obtained from NEA? | ( | ( | ( | If No, please submit plans for DC clearance. If N.A., please provide reasons to support that DC clearance is not required for the proposed development. |
| 5 | Are buildings, sheds, enclosures, structures and equipment to be erected / installed and their intended usage clearly indicated on the plans? | ( | ( | ( | If No, please clearly indicate on the plans. |
| 6 | Are the contents of all storage tanks, materials stored in storage areas or warehouse, and goods / materials handled at loading / unloading areas clearly indicated on the plans? | ( | ( | ( | If No, please clearly indicate on the plans. |
| 7 | Are the processes / activities that will be carried out at the proposed development clearly indicated in the submission proposal? | ( | ( | ( | If No, please include a flow chart diagram / summary showing the processes / activities that will be carried out at the proposed development. |
| Water Pollution Control |
| 1 | Is the trade effluent drainage or piping system used for collecting and conveying the trade effluent generated indicated on the plans? | ( | ( | ( | If No, please clearly indicate on the plans. |
| 2 | Is there any trade effluent treatment plant included in the proposal? | ( | ( | ( | If Yes, please clearly indicate the location of the trade effluent treatment plant on the plans. Please also endorse on the plans that technical details of the trade effluent treatment plant will be submitted separately to PUB(Water Reclamation Network Department) for approval prior to applying for TOP/CSC clearance. |
| 3 | Is the location of trade effluent sampling sump / system (if required) and the connection to the internal sanitary drainage system indicated on the plans? | ( | ( | ( | If No, please clearly indicate on the plans. |
| 4 | Is a pH monitoring system and effluent control system installed at the last inspection chamber (IC) of the proposed development? | ( | ( | ( | If Yes, please clearly indicate the location of the pH monitoring system and effluent control system at the last IC on the plans. Please also endorse on the plans that technical details of the pH monitoring and effluent control system will be submitted separately to PUB(Water Reclamation Network Department) for approval prior to applying for TOP/CSC clearance. |
| 5 | Are the open process areas (which may contaminate the rain water) and the system to collect contaminated rain water for treatment before discharge into the open drain indicated on the plans? | ( | ( | ( | If No, please clearly indicate on the plans. |
| Air Pollution Control |
| 1 | Are types and locations of fuel burning equipment / chimney(s) for the dispersion of flue gases indicated on the plans? | ( | ( | ( | If No, please clearly indicate on the plans and also endorse on the plans that technical details of the fuel burning equipment and chimney will be submitted separately to DCD for approval. |
| 2 | Are the locations of air pollution control equipment and the stacks for the dispersion of exhaust gases indicated on the plans? | ( | ( | ( | If No, please clearly indicate on the plans and also endorse on the plans that technical details of the air pollution control equipment and chimney will be submitted separately to DCD for approval. |
| 3 | Are the chimney(s) and exhaust stack(s) to be installed facing any neighbouring premises? | ( | ( | ( | If Yes, please note that all chimney(s) and exhaust stack(s) shall be properly positioned such that they are not facing directly towards any neighbouring premises and causing public nuisance. |

| Chemical / Oil Storage Facilities |
| --- |
| 1 | Is full containment facility provided for all underground and aboveground bulk storage tanks, including skid tanks? | ( | ( | ( | If No, please note that full containment facility shall be provided. The capacity of the containment facility shall not be less than the capacity of the largest tank. Please also provide the supporting calculations to verify the storage capacity. |
| 2 | Is secondary containment facility (if any) provided with measures to contain shooting jet of chemical / oil during a tank rupture scenario from an elevated storage tank? | ( | ( | ( | If No, please refer to the Singapore Standard on Code of Practice for Pollution Control (i.e. SS593:2013) Section 11.2.4 for the requirements for secondary containment facility. |
| 3 | Are there separate to rainwater discharge systems for all secondary containment facilities which are exposed to weather? | ( | ( | ( | If No, please refer to the Singapore Standard on Code of Practice for Pollution Control (i.e. SS593:2013) Section 11.2.4 for the requirements for secondary containment facility. |
| 4 | Is a leak detection system with alarm provided for all fully enclosed secondary containment facility? | ( | ( | ( | If Yes, please indicate clearly on the plans and also endorse on the plans that a leak detection system with alarm will be provided within the secondary containment facility. |
| Toxic Industrial Waste |
| 1 | Is the location of the toxic industrial waste treatment and disposal facility indicated on the plans? | ( | ( | ( | If No, please clearly indicate on the plans and also endorse on the plans that technical details of the toxic industrial waste treatment and disposal facility will be submitted separately to DCD for approval. |
| Noise Pollution Control |
| 1 | Does the noise generated from the proposed industrial development comply with the permissible noise limits stipulated in the Environmental Protection and Management (Boundary Noise Limits for Factory Premises) Regulations? | ( | ( | ( | Noise generated from the proposed industrial development shall comply with the permissible noise limits stipulated in the Environmental Protection and Management (Boundary Noise Limits for Factory Premises) Regulations. |

Checklist-PC-(Sep 2020)